## Slide 1: Modern Sequencing Technologies
Alan R. Lemmon

## Slide 2: Advances in DNA Sequencing

## Slide 3: 1995

## Slide 4: 2005

## Slide 5: 2018

## Slide 6: Components of High-Throughput Sequencing
DNA Isolation
Fragmentation
Adapter Ligation
Indexing
Quantification
Isolation
  Bead
  Flow cell
  Well
Amplification
  Emulsion PCR
  Bridge Amplification
  None
Sequencing / Signal Detection
  Light
  pH
  Current
Base Calling
Output File

## Slide 7: Emulsion-PCR based Sequencing
454 Sequencing
  https://www.youtube.com/watch?v=KzdWZ5ryBlA
Ion Torrent Sequencing
  https://www.youtube.com/watch?v=DyijNS0LWBY
  Homopolymer error

## Slide 8: Illumina
https://www.youtube.com/watch?v=fCd6B5HRaZ8
Search “Illumina Sequencing by Synthesis” in youtube
Sonication/Nebulization
Adapter Ligation
Isolation - Lawn of adapter oligos in flow cell
Bridge Amplification (generate Clusters), Cluster density
Sequencing by synthesis, with competitive nucleotide incorporation (low indel error)
Color used to call base (laser)
Note two sided flow cell
Output depends on platform , up to PE 250bp paired**
Cost per GB: ~$10
Onboard vs. c-bot clustring
2 vs 8 lane flow cells
Cost of machine = $600k+
MiSeq, HiSeq2500, HiSeq3000/4000, HiSeqX, NovaSeq
Patterned Flow Cells

## Slide 9: Pacific Biosciences
VIDEO http://www.youtube.com/watch?v=v8p4ph2MAvI
Sonication / Nebulization
Isolation
Sequencing by Synthesis, real-time, single molecule
light detection (colored)
25k reads, each ~1000+ bp
Cost of 1 run = $99
Cost of machine = $800k
PacBio Sequel System now available
    7x increase data per run

## Slide 10: Oxford Nanopore
VIDEO:
  https://www.youtube.com/watch?v=hs0FdiTHMbc
  https://www.youtube.com/watch?v=GUb1TZvMWsw
MinION –
USB-key sized sequencer
  $1000 for machine
  100 pores
  2-5kb avg length (max 100kb)
  Error rate = 40%
PromethION –
High througput sequencer
  144,000 pores

## Slide 11: Oxford Nanopore

## Slide 12
MinION
1000x the price
20x the error
New PacBio
100x the price

## Slide 13: Trade-offs
Quantity vs. Read Length vs. Quality
Sources of Constraints
  Asynchrony (all multi-molecule sequencers)
  Strand confusion
*454 / Ion => multiple library fragments per bead
Illumina => cluster mixing
Low Signal
Pacific Biosciences
Oxford Nanopore
NOTE: Cost constraints shifting from collecting sequence data to library preparation and downstream analysis

## Slide 14: Get updates on Sequencing
http://omicsomics.blogspot.com